## Slide 1
Selecting, Constructing,
Operating and Maintaining
High Performance 6 Meter Yagis
Frank Donovan
W3LPL
donovanf@erols.com
11 element
6 meter Yagi
50 feet high
at W3LPL

## Slide 2
home.arrl.org/action/Store/Product-Details/productId/114288
The Most Valuable Investment for any Antenna Builder

## Slide 3
Forget Everything You
Know about HF Propagation
6 Meter Mid-Latitude
Sporadic-E (Es) Propagation is Fundamentally Different

## Slide 4: Northern Hemisphere 6 Meter Mid-Latitude Es Propagation
This presentation focuses exclusively on
northern hemisphere 6 meter mid-latitude Es propagation
- Es as used in this presentation always refers only to
northern hemisphere 6 meter mid-latitude Es propagation
Southern hemisphere 6 meter mid-latitude Es propagation is very similar in almost all respects
- it has unique characteristics not covered in this presentation
Two other common forms of 6 meter Es propagation have
important unique characteristics not covered in this presentation
- equatorial Es every day near the geomagnetic equator
- auroral-E (auroral-Es) only during severe geomagnetic storms
Antenna recommendations in this presentation fully apply
to most forms of 6 meter long distance propagation:
- TEP, F2, FAI, meteor scatter and meteor showers
- ideal antennas for auroral and iono-scatter are slightly different

## Slide 5: Mid-Latitude Es Propagation Below the MUF propagation 800 to 1200 km Near the MUF propagation 1200 to 2000 km Above the MUF propagation 2000 to 10,000+ km
Receiver
Sporadic-E Patch
Sporadic-E Patch
Below
the MUF
Maine 800 km
Above the MUF
Maryland
Above
the MUF
Europe and Asia
4500 to 10,000+ km
Multiple irregularly spaced thin, dense, small, localized Es patches
Newfoundland
2000 km
Above
the MUF
chordal hop
Near the MUF
Elevation angle
usually below 8º
50 ft high
Yagi
Above
the MUF
chordal hop

## Slide 6: Single Hop Es Propagation By far the most common Es propagation
Receiver
Very efficient below and near the MUF reflection from
a thin (about 1 to 2 km thick), small (about 100 km wide or less)
dense, localized Es ionization patch
about 100-110 km (65 miles) above the Earth
Usually about 1500 to 2000 km (1000 to 1200 miles) Occasionally about 800 to 2400 km (500 to 1500 miles)
Near the MUF
Below the MUF
Cuba
2000 km
Maryland
Elevation angle usually below 8º
50 ft high
Yagi
Georgia1000 km

## Slide 7: Double Hop Es Propagation Usually about 2800 to 4000 km (1600-2400 miles) Sometimes as short as 2200 km (1400 miles)
Receiver
Sporadic-E Patch
Sporadic-E Patch
Lossy
intermediate ground reflection
Maryland
California
4000 km
Elevation angle
usually below 5º
50 ft high
Yagi
Kansas
2000 km
Two localized, irregularly spaced, irregularly shaped Es patches

## Slide 8: Above-the-MUF Partial Reflections via Chordal Hops between Es Patches 2000 km (1200 miles) to 10,000+ km (6000+ miles)
Es ionization patches are often capable of efficient above-the-MUF partial reflection at higher frequencies than reflections returning to Earth
Partial reflections may propagate between two or more Es ionization patches via chordal hops with no lossy intermediate ground reflection
Receiver
No (or few)
lossy intermediate ground reflections
One or more chordal hop(s)
Hawaii
Europe
Africa
Asia
Elevation angle
usually below 5º
Maryland
Multiple localized, irregularly spaced, irregularly shaped Es patches
50 ft high
Yagi

## Slide 9: Why is Mid-Latitude Es Very Different? High temperature ablation ionizes the daily influx of many tons of metallic meteoroid dust. Vertical wind shears and tidal winds concentrate the ions into thin dense patches. Electrons move to the ions along magnetic field lines, forming Es patches
Receiver
Seasonally varying diurnal high altitude westerly winds
a few km above the diurnal easterly winds
Wind shears
Wind shears
Thin dense
patches of ions
and electrons in the wind shear null
researchgate.net/publication/227207773_A_Tutorial_Review_on_Sporadic_E_Layers
Wind shear null
Seasonally varying diurnal high altitude easterly tidal winds
at about 95 to 110 km altitude
Tidal winds
Travelling ionospheric disturbances (TIDs)
Ionosphere D Region
50 to 95 km altitude
Ionosphere D Region
50 to 95 km altitude
Tidal wind variability:
minutes to hours
12 hours
24 to 48 hours
many days
seasonal
Tidal winds
Travelling ionospheric disturbances (TIDs)
Electrons can move only along magnetic field lines
High temperature ablation of
tons of metallic meteoroids

## Slide 10: Observed 12 Hour Variability of June-July Es Patch Occurrence at 50-55º North Latitude
Altitude - km
Image credit: GFZ German Research Centre for Geosciences
Local time at the Es ionization patch
midnight
xx
0
3
6
9
12
15
18
24
21
95
100
105
110
115
Evening Es patches
12 hour variability of June-July Es occurrence is caused by
downward drift of high altitude winds towards the D region
Es is most frequent between 7 a.m and 1 p.m. local time
Dense D region below 95 km
6 pm
dawn
midnight
7 am
9 am
10 am
noon
11 am
1 pm
10 pm
8 pm
8 am
3 pm
4 pm
5 pm
10
20
30
40
5
15
25
35
Es Occurrence rate (%)
Daytime Es patches

## Slide 11: Increased Meteor Count at Northern Latitudes from Mid-May to Mid-August Correlates to increased Es Vertical Incidence Critical Frequency
Jan
Mar
May
Aug
Oct
Dec
2000
4000
6000
8000
5.0 MHz
4.5 MHz
4.0 MHz
3.5 MHz
3.0 MHz
2.5 MHz
Average Daily Meteor Count
Average Daily
Vertical Incidence Critical Freq FoEs

## Slide 12
12
Normalized Meteoroid Count Rate
3
4
5
6
Normalized Meteor Count Rate
2
0
Local time at your location
24
18
12
6
Unlike rapidly recombining atmospheric ions, heavy metallic ions ablated from meteoroids
recombine very slowly in the thin E region
and persist for many hours to a day or more
after the 4 to 8 a.m. peak meteoroid influx
The optimum time for meteor scatter
from ionized meteor trails in the E region
is at about 4 to 8 a.m. local time when
your sunrise faces the incoming meteor influx
Facing away from the meteor
influx near your local sunset

## Slide 13: Easily Observable Basic Characteristics of Mid-Latitude Es Propagation
Typical propagation Several thousand square miles
ground footprint to about ten thousand square miles or more
MUFs >50 MHz MUFs every day in June and July
-- but not everywhere and every day --
4000 to 10,000+ km Many days during June and July
Es propagation - a few days in late May and early August
- a few days in late December/early January
Preferred antenna 3 to 6 (or more) element Yagi
Preferred polarization Horizontal polarization is strongly preferred
Preferred heights 50 to 60 feet high (70 feet only for DX)
Compromise height 25 feet high: about 3 dB worse at 1000 km
can be degraded by about 6 dB worse at 2000 km
dense housing and compared to 50 foot height
dense forests within 1000 feet

## Slide 14: Easily Observable Extreme Variability of Mid-Latitude Es Occurrence and Patch Locations
Monthly peak Every day during June and July
occurrence - but not everywhere and every day
Many days in late May and early August Some days in December, January and April
Uncommon from late January to early March
Daily maximum 7 a.m. to noon local time at the Es patch
Es occurrence rate during June and July
Daily peak 6 a.m. to 3 p.m. and 6 p.m. to midnight
Es occurrence rate local time at the Es patch during June and July
Short term Seconds, minutes and hourly variability
Es patch drift Typically drift northward at up to 100 mph
Es patch locations Seconds to minutes to hourly variability
Day-to-day Extreme day-to-day patch location variability
Day-to-evening Extreme day-to-evening location variability

## Slide 15
Optimum Antenna Heights
and Elevation Angles
for 6 Meter Es Propagation
(thanks K9LA)
https://k9la.us/Jul18_Elevation_Angles_Required_for_6m_Sporadic_E.pdf
Antenna Elevation Angles | Single Hop Es Distance | RequiredFoEs (MHz) | Approx Es MUF (MHz) | Optimum Antenna Height
Below 5º | 1400-2300 km | 9-10 | 45-50 | 70 feet
5º to 8º | 1200-1400 km | 10-11 | 50-55 | 50 feet
8º to 12º | 800-1200 km | 11-13 | 55-65 | 25 feet
12º to 15º | 700-800 km | 13-15 | 65-75 | 17 feet
Es MUF infrequently exceeds 60 MHz, limiting Es elevation angles to below 8º
Multi-hop and chordal hop Es occur most frequently at elevation angles below 5º
Yagis higher than about 100 feet are much too high for almost all Es propagation
Few QSO partners have antennas with useful response below about 3º elevation
Frequent
Very Frequent
Not Frequent
Rare
Occurrence

## Slide 16
Horizontal Polarization
Provides up to 6 dB
of “free” ground reflection gain
Vertical polarization provides negligible ground reflection gain
4 to 6 dB of ground reflection gain is routinely achieved
by a horizontally polarized 6 meter antenna unless there:
  - are many tall buildings in front of the antenna
  - is a dense forest of tall trees in front of the antenna
  - is extremely irregular terrain in front of the antenna
Just a few dB of ground reflection gain is rarely achieved
by vertically polarized 6 meter antennas
Horizontal polarization significantly reduces RFI
6 meter RFI sources tend to be vertically polarized

## Slide 17
The Reference Antenna
for Yagi Antenna Gain (dBd)
in this Presentation is the
Half Wavelength Dipole in Free Space
A half wavelength dipole in free space has 2.15 dB gain over an isotropic radiator
Half Wavelength Dipole
in free space
Theoretical Isotropic Radiator

## Slide 18
d
3 dB gain at ~1200 km
8º elevation angle
3 dB gain at ~1800 km
3º elevation angle
6 dB gain at ~1500 km
5º elevation angle
-5 dB
Elevation Pattern and Ground Gain
5 element 6 meter horizontal Yagi 50 ft high Excellent height for almost all Es
Degraded by dense housing within 2000 ft
(roughly more than one house per acre)
low angle lobe
>20º angles
not usable for Es
EZNEC elevation pattern
rarely useful at ~700-1000 km
15º elevation angle

## Slide 19
d
6 dB gain at ~1700 km
4º elevation angle
-5 dB
FIRST FRESNEL ZONE
high angles not usable
for Es
3 dB gain at ~1400 km
6º elevation angle
3 dB gain at ~2000 km
2º elevation angle
rarely useful at ~800-900 km
12º elevation angle
Elevation Pattern and Ground Gain
5 element 6 meter horizontal Yagi 70 ft high
1 to 2 dB better for Es DX than 50 feet high
Only minor degradation by dense housing
Unwanted deep null at 6º to 10º elevation
-5 dB
>20º angles
not usable for Es
low angle lobe
EZNEC elevation pattern

## Slide 20
d
3 dB gain at ~800 km
12º elevation angle
3 dB gain at ~1500 km
5º elevation angle
6 dB gain at ~1000 km
10º elevation angle
-5 dB
>20º angle
not usable for Es
Elevation Pattern and Ground Gain
5 element 6 meter horizontal Yagi 25 ft high
Adequate height if you can’t go higher
Only 3 to 6 dB worse than 50 foot height
Degraded by dense housing within 1000 feet
(roughly more than one house per acre)
low angle lobe
zz
EZNEC elevation pattern

## Slide 21
d
Elevation Pattern and Ground Gain
5 element 6 meter horizontal Yagi 100 ft high
Too high for almost all Es propagation
Unwanted deep null at 4º to 7º elevation
6 dB gain at ~1800 km
3º elevation angle
3 dB gain at ~1500 km
4º elevation angle
3 dB gain at ~2100 km
1º elevation angle
-5 dB
>20º angles
not usable for Es
rarely useful at 700-1000 km
14º elevation angle
EZNEC elevation pattern
x
low angle lobe

## Slide 22
d
Front to Rear (F/R) Ratio
Maximum signal from the front
of the antenna
Maximum signal from the rear
of the antenna
front
rear

## Slide 23
6 dBd Ground Gain of a Horizontal 1/2 Wave Dipole with
Only Minor Irregularities in the Reflection Zone
Terrain irregularities: <25% of antenna height
Dense housing: <25% of antenna height
Dense forest: <25% of antenna height
Obstructing less than 5% of the reflection zone
A horizontal half wave dipole at least 0.5 wavelength high with relatively smooth terrain and few tall buildings in the reflection zone has 6 dBd gain over a horizontal dipole in free space
dBi
dBi
dBi

## Slide 24
IN-PHASE REFLECTED RAY
DIRECT RAY
IMAGINARY
IMAGE ANTENNA
.
.
.
.
.
.
SINGLE POINT GROUND REFLECTION
WITH NO OBSTRUCTIONS
AND NO IRREGULAR TERRAIN
The Classic “Image Antenna” Model
an accurate model
for computing peaks and nulls
in antenna elevation patterns
But it assumes an ideal ground reflection
with no obstructions and no irregular terrain
.
.
.

## Slide 25
What is the Actual Reflecting Zone
in front of my antenna?
It definitely is not just a single point!
MANY REFLECTED RAYS
DIRECT RAY
How wide is the reflection zone?
How far in front of my antenna is the reflection zone?
How long is the reflection zone?
How much do obstructions degrade ground reflection gain?
How much does irregular terrain degrade ground reflection gain?

## Slide 26
The Fresnel Zone
By definition includes all ground reflections
within +/- 90º of the phase of the direct ray that
add to the power from the direct ray if ground
reflections are not obstructed or absorbed
DIRECT RAY
ONLY ONE REFLECTED RAY
IS EXACTLY IN-PHASE
WITH THE DIRECT RAY
FRESNELZONE
EDGE
https://ia801604.us.archive.org/5/items/sitingcriteriafo139utla/sitingcriteriafo139utla.pdf
+6 dB
ground gain
0 dB
ground gain
0 dB
ground gain

## Slide 27
d
The Fresnel Zone
Unobstructed 0º to 45º phase shifted reflections from roughly the middle half of the Fresnel zone contribute more power to low angle radiation than the 45º to 90º phase shifted reflections
from roughly the outer half of the Fresnel zone
DIRECT RAY
IN-PHASE REFLECTED RAY
FRESNEL
ZONE
EDGE
+6 dB
45º PHASE SHIFTED REFLECTED RAYS
+0 dB
+0 dB
90º PHASE SHIFTED REFLECTED RAYS

## Slide 28
+3 to +6dB Ground Reflection Zone
is roughly in the middle half of the Fresnel zone
Ideally the reflection zone should not be obstructed by
- tall buildings and forests occupy < 5% of the zone
- buildings and forests are < 25% of antenna height
- irregular terrain < 25% of antenna height
DIRECT RAY
Roughly the middle half of the Fresnel zone
forms the -3 dB contour of the antenna’s low angle lobe
IN-PHASE REFLECTED RAY
+3 dB
+3 dB
+6 dB
+0 dB
+0 dB

## Slide 29
d
+3 to +6dB Ground Reflection Zone
6 meter horizontal Yagi 50 feet high
5º elevation angle
+3 to +6 dB
reflection zone
+3 dB
DIRECT RAY
~150 ft
~2000 ft
IN-PHASE REFLECTED RAY
+3 dB
~200 ft
+ 0 dB
+0 dB
+6 dB

## Slide 30
d
+3 to +6dB Ground Reflection Zone
6 meter horizontal Yagi 70 feet high
4º elevation angle
+3 to +6 dB
reflection zone
+3 dB
DIRECT RAY
~200 ft
~2500 ft
IN-PHASE REFLECTED RAY
+3 dB
~250 ft
+0 dB
+0 dB
+6 dB

## Slide 31
d
+3 to +6dB Ground Reflection Zone
6 meter horizontal Yagi only 25 feet high
10º elevation angle
+3 to +6 dB
reflection zone
+3 dB
DIRECT RAY
~25 ft
~1000 ft
IN-PHASE REFLECTED RAY
+3 dB
~100 ft
+0 dB
+0 dB
+6 dB

## Slide 32
d
5º Sloping Terrain in the Reflection Zone
6 meter horizontal Yagi 25 feet high
~100 ft of sloping terrain over ~1000 ft
5º elevation angle
+3 to +6 dB
reflection zone
+3 dB
DIRECT RAY
~25 ft
~1000 ft
IN-PHASE REFLECTED RAY
+3 dB
~100 ft
+0 dB
+0 dB
+6 dB

## Slide 33: High Performance Short Yagis Light weight and small wind area Yagis Gain and front-to-rear ratio Source: VE7BQH charts (December 13, 2021)
  Type Elements Gain Front to Boom Cost dBd Rear Ratio Length
  M2 6M3 3 6 13 dB 7 ft $299
  EAntenna 50LFA4 4 7 21 10 $260
  Directive Sys JX5-50 5 8 17 13 $240
  YU7EF EF0605C 5 8 24 14 -
  G0KSC 4.4m 5LFA 5 8 19 14 $225+
  EAntenna 50LFA5 5 8 21 14 $300
www.dxmaps.com/ve7bqh6.html

## Slide 34: M2 6M3 Lightweight Yagi 3 Element T-matched Yagi 7 Foot Boom 6 Pounds 6 dBd Gain 13 dB F/R Ratio
www.m2inc.com/content/PDF%20MANUALS/6MANTS/6M3MAN03-W.pdf

## Slide 35: EAntenna 50LFA4 4 Element Loop Fed Yagi 10 Foot Boom 13 Pounds 7 dBd Gain 21 dB F/R Ratio
www.dxengineering.com/parts/ean-r2010106

## Slide 36: EAntenna 50LFA5 5 Element Loop Fed Yagi 14 Foot Boom 17 Pounds 8 dBd Gain 21 dB F/R Ratio
www.dxengineering.com/parts/ean-r2010102

## Slide 37: YU7EF EF0605C 5 element split dipole feed Yagi 14 Foot Boom 17 Pounds 8 dBd Gain 24 dB F/R Ratio
www.yu7ef.com/ef0605c.htm

## Slide 38: G0KSC 5LFA 5 Element Loop Fed Yagi 14 Foot Boom 13 Pounds 8 dBd Gain 19 dB F/R Ratio
www.g0ksc.co.uk/50mhz-lfa-yagis/5el-44mtr-boom-lfa.html

## Slide 39: Higher Performance Long Yagis Significantly improved front-to-rear ratio Gain and front-to-rear ratio Source: VE7BQH charts (December 13, 2021)
  Type Elements Gain Front to Boom Cost
  dBd Rear Ratio Length
  G0KSC 6.2m 6LFA 6 9 30 dB 21 ft $406+
  Innov 6.83m 6LFA 6 10 27 22 $447+
  EAntenna 50LFA6 6 10 27 23 $460
  G0KSC 8.9m 7LFA 7 11 25 29 $554+
  EAntenna 50LFA7 7 11 26 31 $500
  M2 6M7JHV 7 11 21 31 $525
  Innov 8LFA 8 11 29 39 $812+
www.dxmaps.com/ve7bqh6.html

## Slide 40: G0KSC 6LFA 6 Element Loop Fed Yagi 21 Foot Boom 14 Pounds 9 dBd Gain 30 dB F/R Ratio
www.g0ksc.co.uk/50mhz-lfa-yagis/6el-64mtr-boom-lfa.html

## Slide 41: InnovAntennas 6.83m 6LFA 6 Element Loop Fed Yagi 22 Foot Boom 14 Pounds 10 dBd Gain 27 dB F/R Ratio
www.g0ksc.co.uk/50mhz-lfa-yagis/6el-64mtr-boom-lfa.html

## Slide 42: Eantennas 50LFA6 6 Element Loop Fed Yagi 23 Foot Boom 30 Pounds 10 dBd Gain 27 dB F/R Ratio
www.dxengineering.com/parts/ean-r2010108

## Slide 43: G0KSC 8.9m 7LFA 7 Element Loop Fed Yagi 29 Foot Boom 33 Pounds 11 dBd Gain 25 dB F/R Ratio
www.g0ksc.co.uk/7el-low-noise-lfa.html
W7EW 180 foot tower

## Slide 44: Eantennas 50LFA7 7 Element Loop Fed Yagi 31 Foot Boom 50 Pounds 11 dBd Gain 26 dB F/R Ratio
www.dxengineering.com/parts/ean-r2010111

## Slide 45: M2 6M7JHV 7 Element T-matched Yagi 26 Foot Boom 18 Pounds 11 dBd Gain 21 dB F/R Ratio
static.dxengineering.com/global/images/instructions/msq-6m7jhv.pdf

## Slide 46: InnovAntennas 8LFA 8 Element Loop Fed Yagi 38 Foot Boom 40 Pounds 11 dBd Gain 29 dB F/R Ratio
innovantennas.com/en/shop-page/190/3/vhf-uhf-ham-radio-antennas/50mhz-yagis-all/8-element-50mhz-lfa2-yagi-11-67mInnovAntennas%20shop.html
JA1BK

## Slide 47: Yagi Element Construction
Center of each Yagi element:
6 feet of 0.5” diameter x 0.058” wall aluminum tubing
dxengineering.com/parts/dxe-at1205
Tips of each Yagi element:
2 feet of 0.375” diameter x 0.058” wall aluminum tubing
dxengineering.com/parts/dxe-at1189

## Slide 48: Protecting Yagi Element Joints Anti-Sieze and Anti-Corrosion Lubricant
Assures RF conductivity
Prevents oxidation and corrosion
No long-term drying and caking like many other lubricants
Effortless Yagi element disassembly
Effortless parts cleaning
dxengineering.com/parts/jtl-12555

## Slide 49: Yagi Boom Construction
12 foot boom: Two 6 ft x 1.5” o.d. x 0.058” wall aluminum tubing
dxengineering.com/parts/dxe-at1488
18 foot boom: Three 6 ft x 1.5” o.d. x 0.120” wall aluminum tubing
dxengineering.com/parts/dxe-at1311
24 foot boom: Four 6 ft x 2” o.d. x 0.058” wall aluminum tubing
dxengineering.com/parts/dxe-at1492
Square aluminum tubing makes precise element levelling easier
use 1.5 inch square tubing for a 12 foot boom
use 2.0 inch square tubing for a 24 foot boom
metalsdepot.com/aluminum-products/aluminum-square-tube

## Slide 50: Stauff Clamps For mounting Yagi elements to a horizontal plate attached to a Yagi boom
wilson-company.com/product/30127pp/two-bolt-heavy-duty-clamp-body-only

## Slide 51: RFI Suppression Choke necessary at the feed point of a Yagi split driven element
Unbalanced driven element current
degrades Yagi sidelobe performance
innovantennas.com/en/baluns-why-do-i-need-one.html
www.ifwtech.co.uk/g3sek/in-prac/inpr1005_ext_v2.pdf
RFI received as common mode current on the outside of the coaxial cable shield degrades
Yagi sidelobes and
front-to-rear performance
driven element
driven element

## Slide 52: RFI Suppression Choke Coiled RG-213 Resonant Choke suitable for quiet RFI environments
Four turns of RG-213 wound on a 2.5 inch diameter form The builder must measure for choke resonance near 50 MHz
Space the choke a few inches from the boom
to preserve RFI suppression performance
Close wound

## Slide 53: RFI Suppression Choke 20 Mix-31 Round-Cable Ferrite Cores Installed over RG-213 Suitable for most RFI environments
innovantennas.com/index.php?option=com_content&view=article&id=3&Itemid=189&lang=en
Space the choke a few inches from the boom
to preserve RFI suppression performance
DX Engineering DXE-CB31-500-10 ferrite cores
dxengineering.com/parts/dxe-cb31-500-10
myantennas.com/wp/product/cmc-154-3k

## Slide 54: RFI Suppression Choke Five Mix-31 Clamp-On Ferrite Beads Optimized for severe RFI environments
audiosystemsgroup.com/ChokesVHF.pdf
before installation
K9YC

## Slide 55: Low Loss Coaxial Cable Really pays off on 6 meters
RG-8X flexible coax 40 feet per dB
RG-213 flexible coax 60 feet per dB
LDF4-50A 1/2” hardline 200 feet per dB
3/4” CATV 75 Ω hardline 275 feet per dB
LDF5-50A 7/8” hardline 400 feet per dB
LDF4-50A has one dB less loss than RG-213
at a cable length of only 85 feet
LDF4-50A has two dB less loss than RG-213
at a cable length of only 170 feet
LDF5-50A has one dB less loss than LDF4-50A
at a cable length of 475 feet

## Slide 56: Reliable Coaxial Cable Connectors for 6 Meters
N and UHF connectors are commonly used
  both have insignificant measured loss on 6 meters
High quality silver plated PL-259 UHF connectors
  much more reliable center pin mating force than N connectors
Common N connector failures caused by pin installation errors
  unreliable mating caused by insufficient pin length and pin pullback
  damage caused by excess pin length and axial pin misalignment
Captive pin N connectors solve N connector reliability issues
  assures the necessary +/- 0.020 inch (+/- ½ mm) pin depth tolerance
  prevents connector damage caused by pin misalignment
  prevents unreliable connection caused by pin pullback
Avoid using adapters as much as possible
  use only name-brand silver plated adapters
  never use nickel plated or “astro-plated” connectors and adapters
  never use cheap import “no name” adapters and connectors
Gently wrench tighten all of your PL-259 connectors (~1/4 turn)
Avoid saving a few dollars on cheap unbranded coaxial cable connectors and adapters

## Slide 57: Amphenol 83-1SP PL-259 UHF Male Connector
Silver Plated Center Pin
Silver Plated Body
Shell is labeled exactly:
Amphenol 83-1SP
newark.com/amphenol-rf/83-1sp/rf-coaxial-uhf-plug-straight-50ohm/dp/59K0534
Amphenol 83-1SP: an excellent coaxial connector for 6 meters

## Slide 58: Its Very Easy to Waterproof your RG-213 Coaxial Cable to preserve the life of your coax
Scotch 130C rubber tape covered by Scotch 33+ electrical tape
Heavy electrical solder lugs
No exposed coax braid, dielectric or center conductor
Water and moisture intrusion is the enemy of low coaxial cable loss

## Slide 59: Yagi Driven Element Waterproof, shakeproof and corrosion resistant driven element connections
Stainless steel
external tooth lockwasher
Heavy electrical solder lugs not in direct contact with aluminum tubing
Stainless steel
nylon insert “Nyloc” locknut
Stainless steel screw
Firmly fasten your coax to the boom to prevent vibration
Scotch 130C
rubber tape covered by Scotch 33+ electrical tape

## Slide 60: Driven Element Connections Waterproof and Corrosion Resistant
dxengineering.com/parts/pld-let14z03
Liquid electrical tape

## Slide 61: Inexpensive Materials for Waterproofing your Connectors
Cover your connectors with two 50% overlapped layers
of Scotch 130C self-vulcanizing linerless rubber splicing tape
- stretch to 50% of its original width until it changes color
- sticky side facing out
homedepot.com/p/3M-Scotch-3-4-in-x-30-ft-Linerless-Rubber-Splicing-Tape-41717-BX-10/205523418
Cover Scotch 130C rubber tape with two 50% overlapped layers
of Scotch Super 33+ vinyl electrical tape
homedepot.com/p/Scotch-Super-33-3-4-in-x-66-ft-x-0-007-in-Vinyl-Electrical-Tape-Black-6132-BA-10/304653556